## Slide 1: Descriptive and inferential statistical methodologies have proven effective in creating a proactive ‘alarm’, accurately identifying Pump Failures with Horse Power (HP) and Pump Efficiency (PE) emerging as key variables of interest with deviations of 15 HP and > 3 % PE being our core signal thresholds.

## Slide 2: Descriptive Analysis has enabled us to clearly identify particular signature abnormalities showing clear signature changes in both Rolling Standard Deviation and Rolling Mean Datasets when observed over the respective failure period of interest.

## Slide 3: Further segmentation of the data via binary means (Pump Failure = 0 or 1) illustrated through Rolling Standard Deviation and Rolling Mean, show a clear signature difference between that of normal behavior and that of Failure with pump torque, pump speed, and pump efficiency showing the 3 largest variances.
Rolling Standard Deviation
(Pump Failure = 1)
Rolling Standard Deviation
(Pump Failure = 0)
Rolling Mean
(Pump Failure = 1)
Rolling Mean
(Pump Failure = 0)

## Slide 4: Correlation analyses across datasets yield interesting insights with pump efficiency and volumetric flow negatively correlated with Pump Failure in the Rolling Mean Dataset, whilst horse power and volumetric flow show a subsequently strong positive correlation in the Rolling Stdev Dataset.
Chart: Correlation Strength Associated With Pump Failure (Rolling Mean 30 Minute)
| Horse Power | Pump Speed (RPM) | Pump Torque | Ambient Temperature | Volumetric Flow Meter 1 | Pump Efficiency | Volumetric Flow Meter 2
 | 0.21803 | -0.18417 | -0.21603 | -0.30265 | -0.69244 | -0.69503 | -0.69773
Chart: Correlation Strength Associated With Pump Failure (Rolling Stdev 30 Minute)
| Horse Power | Volumetric Flow Meter 1 | Pump Efficiency | Volumetric Flow Meter 2 | Pump Speed (RPM) | Ambient Temperature | Pump Torque
 | 0.6901 | 0.64488 | 0.64355 | 0.62592 | 0.62456 | 0.60005 | 0.59726

## Slide 5: Lastly, analysis of the model fit reveals that with a R Squared of 0.78, a linear model is a good fit for the data with horse power, pump efficiency and volumetric flow meter 1 having the largest coefficients, indicative that these variables have the most immediate relationship with respect to Pump Failure behaviour.
Chart: Coefficient Ranking
| Horse Power | Pump Efficiency | Volumetric Flow Meter 1 | Ambient Temperature | Pump Speed (RPM) | Pump Torque | Volumetric Flow Meter 2
 | 0.76485 | 0.34237 | 0.050934 | 0.018207 | -0.017867 | -0.018902 | -0.61136